## Slide 1: Flammability of Hydrogen at Sub-Atmospheric Pressures and Reduced Oxygen Concentrations

## Slide 2: Hydrogen Properties
Gas at room temperature, can displace air
Very wide flammability limits (~4-76% at sea level)
Very low ignition energy needed (<0.1mJ)
In a closed container, explosion pressure rises up to 8 times initial pressure in as little as 10ms
Adiabatic flame temperature of 4010°F (2210°C)

## Slide 3: Objective
Test flammability of hydrogen in air at atmospheric and sub-atmospheric pressures
Pressures replicating elevations of 0, 15,000, 30,000, and 40,000 feet (14.7, 8.29, 4.36, and 2.71 PSI, respectively)
Find flammability limits and verify with previous data
Test flammability properties and in oxygen-depleted air at these pressures (added nitrogen)
Find the limiting oxygen concentration

## Slide 4: Concept
Nitrogen can be added to air to lower the oxygen concentration, effectively inerting the H2-air mixture
Similar to inerting the empty space in jet fuel tank
Allowable oxygen concentration vs. altitude according to AC 25-981-2A

## Slide 5: Common Experimental Methods
From Upper Flammability Limits of Hydrogen and Light Hydrocarbons in
Air at Subatmospheric Pressures, Hai Le, et al. 2012
From Flammability of Methane, Propane, and Hydrogen gases, Kenneth L. Cashdollar, et al. 2000
Variables:
Vessel type
Vessel size
Ignitor type
Ignition energy
Flammability criterion

## Slide 6: Experimental Setup

## Slide 7: Experimental Setup
Based on ASTM standards
20L, ½” thick steel chamber, 300 PSI max
Chamber evacuated, then filled by partial pressures
Can mix hydrogen, nitrogen, and air at any ratio
Initial pressure varied from 2.71 to 14.7 PSI
Initial temperature 72°F (22°C)
Ignited with 15,000V, 30mA continuous spark, 0.5s duration
Considered flammable if pressure rise 3% over initial pressure

## Slide 8: Experimental Setup
High Pressure Transducer
Thermocouple
Electrodes
Picture of explosibility chamber outside and inside

## Slide 9
Chart: Spark Electrode Gap Comparison
Gap (in.) | Avg. Energy (J)
0.186 | 1.09
0.3125 | 1.24
0.625 | 1.65
0.75 | 1.88
Chart: Average Spark Energy in 0.05s Spark
| 0.186 | 0.3125 | 0.625 | 0.75
Avg Energy | 1.0888 | 1.2409 | 1.6549 | 1.8785

## Slide 10: From Literature
Flammability limits are wider with larger spark gap
Final Configuration: 0.65” gap, 0.5s duration, 12.4J average energy
From Minimum ignition energy of hydrogen–air mixture: Effects of humidity and spark duration, Ryo Ono, et. al, University of Tokyo, 2007.

## Slide 11: Example of Single Test Pressure Data
3.62% Pressure Rise, 823 ms Rise Time
Chart: 4.55% H2, 95.45% Air, 8.292 PSIA

## Slide 12: Example of Single Test Pressure Data
Chart: Atmospheric Pressure, Stoichiometric Hydrogen in Air
686% Pressure Rise, 12ms Rise Time

## Slide 13
Chart: H2 Lower Flammability Limit vs. Pressure
| 3.9934689434655418E-2 | 4.0010887316276542E-2 | 4.3194340521052976E-2 | 4.50989728589892E-2 | 4.5361806311207849E-2 | 4.5584433256225361E-2 | 4.6737873324715955E-2 | 4.6809089672064236E-2 | 4.7541318098347267E-2 | 4.8095238095238101E-2 | 4.823457378052929E-2 | 4.8823609411124708E-2 | 4.9054293101102195E-2 | 5.291797034417086E-2 | 5.5854139737397099E-2 | 5.9936050071433447E-2 | 6.0144237311198792E-2
Atmospheric | 0.0090754 | 0.011956 | 0.013088 | 0.022345 | 0.025952 | 0.025861 | 0.024417 | 0.029446 | 0.025995 | 0.035231 | 0.02892 | 0.042173 | 0.044271 | 0.056645 | 0.076713 | 0.090095 | 0.098075
15,000 Feet | 0.0094406 | 0.0093682 | 0.015318 | 0.011449 | 0.021283 | 0.027273 | 0.027732 | 0.028781 | 0.036179 | 0.039759 | 0.044514 | 0.047424 | 0.051423 | 0.068694 | 0.083506 | 0.095575
30,000 Feet | 0.007539 | 0.020266 | 0.021394 | 0.023016 | 0.035348 | 0.034815 | 0.033167 | 0.038705 | 0.044999 | 0.045359 | 0.045054 | 0.049576 | 0.051983 | 0.070386 | 0.09033
40,000 Feet | 0.011411 | 0.012242 | 0.018403 | 0.024935 | 0.026485 | 0.024548 | 0.035693 | 0.039838 | 0.039764 | 0.03792 | 0.04399 | 0.05046 | 0.051251 | 0.055155 | 0.062082 | 0.053614 | 0.074446 | 0.074478 | 0.083694 | 0.090929 | 0.10033
LFL decreased as the altitude increased

## Slide 14
Chart: H2 Upper Flammability Limit vs. Pressure
| 0.75469515514425689 | 0.76420551207893839 | 0.77 | 0.77500340182337735 | 0.77705185790118414 | 0.7798938919874846 | 0.78029891304347831 | 0.78060738117935446 | 0.781194840461643 | 0.78152632294925861 | 0.78215062533985857 | 0.78332993405398055 | 0.78447513436288174
Atmospheric | 2.6593 | 2.4247 | 1.6744 | 0.59884 | 0.15223 | 0.043497 | 0.037486 | 0.03043 | 0.031018 | 0.034181 | 0.028528 | 0.026895 | 0.020913
15,000 Feet | 3.1759 | 2.6917 | 1.4932 | 1.4932 | 0.63281 | 0.59262 | 0.050314 | 0.048561 | 0.041474 | 0.039483 | 0.042543 | 0.039757 | 0.029383 | 0.028724
30,000 Feet | 2.925 | 2.8984 | 2.6947 | 2.677 | 2.6891 | 2.4982 | 0.021747 | 0.020512 | 0.02314 | 0.021854 | 0.022756 | 0.022761 | 0.018441 | 0.017672 | 0.016007 | 0.014813
40,000 Feet | 3.2163 | 3.0142 | 2.6523 | 2.8295 | 0.021848 | 0.022595 | 0.021891 | 0.021373 | 0.019236 | 0.020234 | 0.017417 | 0.0166 | 0.015623 | 0.015938 | 0.012935
Much larger change in pressure rise as H2 concentration changed

## Slide 15
Chart: H2 Upper Flammability Limit vs. Pressure
| 0.7798938919874846 | 0.78029891304347831 | 0.78060738117935446 | 0.781194840461643 | 0.78152632294925861 | 0.78215062533985857 | 0.78332993405398055 | 0.78447513436288174
0 Feet | 0.043497 | 0.037486 | 0.03043 | 0.031018 | 0.034181 | 0.028528 | 0.026895 | 0.020913
15000 Feet | 0.050314 | 0.048561 | 0.041474 | 0.039483 | 0.042543 | 0.039757 | 0.029383 | 0.028724 | 0.028215 | 0.027312
30,000 Feet | 0.021747 | 0.020512 | 0.02314 | 0.021854 | 0.022756 | 0.022761 | 0.018441 | 0.017672 | 0.016007 | 0.014813
40,000 Feet | 0.021848 | 0.022595 | 0.021891 | 0.021373 | 0.019236 | 0.020234 | 0.017417 | 0.0166 | 0.015623 | 0.015938 | 0.012935

## Slide 16
Chart: 40,000 feet (2.71 PSIA) H2 Rich Flammability Limit
| 0.75623167155425219 | 0.76623853211009174 | 0.76832412523020255 | 0.7686885005140256 | 0.76869795888291204 | 0.76889052709178041 | 0.76931567328918327 | 0.76937201615864848 | 0.76982378854625555 | 0.77027027027027029 | 0.77213352685050796 | 0.77221206581352841 | 0.77321814254859611 | 0.77376219732562346
0.5s Spark | 3.2163 | 3.0142 | 2.6523 | 2.8295 | 0.021848 | 0.022595 | 0.021891 | 0.021373 | 0.019236 | 0.020234 | 0.017417 | 0.0166 | 0.015623 | 0.015938
1s Spark | 2.7898 | 2.8488 | 0.022263 | 0.019383
10s Spark | 2.9565 | 2.8848 | 2.6596 | 0.027122 | 0.027139 | 0.029875
Not Enough Spark Energy at Low Pressure Upper Flammability Limits

## Slide 17
Altitude (ft.) | Lower Limit
0 | 4.70%
15,000 | 4.41%
30,000 | 4.07%
40,000 | 3.89%
Altitude (ft.) | Upper Limit
0 | 78.18%
15000 | 78.87%
30000 | 77.86%
40000 | 76.87%
Chart: Hydrogen Upper Flammability Limit in Air
| 0 | 15000 | 30000 | 40000
Upper Limit | 0.7818 | 0.7887 | 0.7786 | 0.7687
Chart: Hydrogen Lower Flammability Limit in Air
| 0 | 15000 | 30000 | 40000
3% Criterion | 0.047 | 0.0441 | 0.0407 | 0.0389
As altitude increased, flammability limits widened except where limited by spark energy

## Slide 18
Pressure (atm) | Altitude (ft.)
1 | 0
0.7 | 9,500
0.5 | 18,000
0.3 | 30,000
0.1 | 52,000
From Lower and Upper Flammability Limits of Hydrogen and Light Hydrocarbons in Air at Subatmospheric Pressures, Hai Le, et al., 2012
From Flammability limits and laminar flame speed of hydrogen-air mixtures at sub-atmospheric pressures, M. Kuznetsov, et al., 2012
Measured flame propagation in 10cm diameter tube
Pressure rise 10× igniter alone in 25cm diameter sphere
Previous Experimental Data

## Slide 19: Inerting with Nitrogen in Literature
Tested in a 6 ft by 2 in diameter tube at atmospheric pressure
Flame did not propagate below 4.9% oxygen concentration
From Limits of Flammability of Gases and Vapors, H. F. Coward and G. W. Jones, Bureau of Mines, 1952.

## Slide 20
Chart: Atmospheric Pressure(14.7PSI) Hydrogen in Oxygen Depleted Air
| 4.6809089672064236E-2 | 4.8095238095238101E-2 | 6.0144237311198792E-2 | 8.0628699734639736E-2 | 0.15077907055861742 | 0.22866594652984065 | 0.29733405875952118 | 0.29733405875952118 | 0.35987780040733197 | 0.45305483739284252 | 0.59869405523058083 | 0.75469515514425689 | 0.76420551207893839 | 0.77500340182337735 | 0.77705185790118414 | 0.7798938919874846 | 0.78215062533985857
0% N2 | 0.029446 | 0.035231 | 0.098075 | 0.4316 | 4.2392 | 6.0426 | 6.8621 | 6.8621 | 6.7738 | 6.1693 | 4.8285 | 2.6593 | 2.4247 | 0.59884 | 0.15223 | 0.043497 | 0.028528
20% N2 | 0.021407 | 0.030892 | 0.038204 | 0.050731 | 0.38903 | 4.3979 | 6.069 | 6.069 | 5.7382 | 4.8063 | 2.4665 | 0.032505 | 0.028347
40% N2 | 0.028523 | 0.033777 | 0.32576 | 3.7082 | 4.9737 | 4.9737 | 4.3047 | 2.8714 | 0.21106 | 0.043897 | 0.033002 | 0.022948
60% N2 | 0.024752 | 0.0323 | 0.31443 | 2.7977 | 2.7977 | 2.178 | 0.65526 | 0.032751 | 0.028858

## Slide 21
Chart: 15,000 feet (8.29PSI) Hydrogen in Oxygen Depleted Air
| 4.3871278775461021E-2 | 4.5465508924264354E-2 | 5.8724225250211037E-2 | 8.0188110454600281E-2 | 0.15241770167611238 | 0.22034715525554485 | 0.29506812974798025 | 0.29506812974798025 | 0.36207936316487754 | 0.41337349397590356 | 0.60043378720327745 | 0.74960876369327079 | 0.77137033928785514 | 0.78576589595375723 | 0.7858176555716353 | 0.78841522157996147
0% N2 | 0.028781 | 0.036179 | 0.095575 | 0.42208 | 4.4186 | 5.7675 | 6.7692 | 6.7692 | 6.6487 | 6.3561 | 4.7641 | 3.1759 | 2.6917 | 0.59262 | 0.050314 | 0.029383
20% N2 | 0.029312 | 0.036792 | 0.41669 | 2.9181 | 5.4271 | 5.967 | 5.967 | 5.6605 | 4.7415 | 3.6786 | 1.7352 | 0.035995 | 0.029786
40% N2 | 0.024451 | 0.034823 | 0.34982 | 3.7261 | 4.8128 | 4.8128 | 4.7104 | 3.6874 | 2.61 | 0.094563 | 0.043116 | 0.033148 | 0.024928
60% N2 | 0.020104 | 0.033482 | 0.35513 | 2.1008 | 3.0773 | 3.0773 | 2.4943 | 0.5195 | 0.032099 | 0.028792

## Slide 22
Chart: 30,000 feet (4.36PSI) Hydrogen in Oxygen Depleted Air
| 3.9461678832116792E-2 | 4.1628959276018083E-2 | 5.2016498625114586E-2 | 8.1310123683005039E-2 | 0.14947271893626773 | 0.22329206785878036 | 0.2959651535992664 | 0.2959651535992664 | 0.35809261806510773 | 0.45050412465627859 | 0.60073260073260082 | 0.76845411711913847 | 0.77862735831042451 | 0.77864166476103358
0% N2 | 0.023016 | 0.033167 | 0.09033 | 0.67169 | 4.1928 | 5.7784 | 6.7463 | 6.7463 | 6.5698 | 5.9302 | 4.7804 | 2.925 | 2.4982 | 0.021747
20% N2 | 0.025418 | 0.03425 | 0.49249 | 3.9131 | 5.3026 | 5.8291 | 5.8585 | 5.8585 | 5.6717 | 4.7624 | 3.6533 | 2.4025 | 0.036956 | 0.015896
40% N2 | 0.025635 | 0.031935 | 0.45807 | 3.6204 | 4.7274 | 4.7274 | 4.6377 | 3.6865 | 2.6224 | 0.64417 | 0.035606 | 0.019584
60% N2 | 0.010834 | 0.032868 | 0.45871 | 2.0733 | 3.078 | 3.078 | 3.0731 | 1.9991 | 0.4791 | 0.050434 | 0.028083

## Slide 23
Chart: 40,000 feet (2.71PSI) Hydrogen in Oxygen Depleted Air
| 3.8731095536702322E-2 | 3.9085545722713895E-2 | 4.9023221525985997E-2 | 8.0265095729013233E-2 | 0.15149281238481388 | 0.22246696035242292 | 0.29500367376928727 | 0.29500367376928727 | 0.36198106336489433 | 0.45119705340699812 | 0.6 | 0.75623167155425219 | 0.7686885005140256 | 0.76869795888291204
0% N2 | 0.026485 | 0.035693 | 0.1174 | 0.77931 | 4.0585 | 5.5737 | 6.4645 | 6.4645 | 6.4128 | 5.8885 | 4.6076 | 3.2163 | 2.8295 | 0.021848
20% N2 | 0.038209 | 0.046372 | 0.57355 | 3.7121 | 5.9077 | 5.9077 | 5.6352 | 4.9901 | 4.2481 | 3.1317 | 2.7318 | 2.472 | 0.019034
40% N2 | 0.035374 | 0.68266 | 1.7074 | 3.389 | 4.6158 | 4.6158 | 4.2787 | 3.5532 | 2.3402 | 0.3286 | 0.053636 | 0.029202
60% N2 | 0.011123 | 0.040642 | 0.62544 | 2.9681 | 3.0163 | 3.1599 | 3.1599 | 3.1032 | 2.9676 | 1.801 | 0.056955 | 0.048177 | 0.037075 | 0.031261 | 0.028976

## Slide 24
Chart: Hydrogen Explosion Pressure Increase at Varying Altitudes and Nitrogen Concentrations
| 4.6809089672064236E-2 | 4.8095238095238101E-2 | 6.0144237311198792E-2 | 8.0628699734639736E-2 | 0.15077907055861742 | 0.22866594652984065 | 0.29733405875952118 | 0.29733405875952118 | 0.35987780040733197 | 0.45305483739284252 | 0.59869405523058083 | 0.75469515514425689 | 0.76420551207893839 | 0.77500340182337735 | 0.77705185790118414 | 0.7798938919874846
Sea Level, 0% N2 | 0.43286 | 0.5179 | 1.4417 | 6.3445 | 62.3156 | 88.8256 | 100.8724 | 100.8724 | 99.5744 | 90.6888 | 70.9793 | 39.0924 | 35.6425 | 8.8029 | 2.2377 | 0.63941 | 0.41936
Sea Level, 20% N2 | 0.31469 | 0.45411 | 0.5616 | 0.74575 | 5.7188 | 64.6498 | 89.2136 | 89.2136 | 84.3519 | 70.6527 | 36.2574 | 0.47783 | 0.4167
Sea Level, 40% N2 | 0.41929 | 0.49652 | 4.7887 | 54.5105 | 73.1129 | 73.1129 | 63.2794 | 42.2098 | 3.1025 | 0.64529 | 0.48513 | 0.33734
Sea Level, 60% N2 | 0.36385 | 0.4748 | 4.6221 | 41.1262 | 41.1262 | 32.0166 | 9.6323 | 0.48144 | 0.42421
15,000 Feet, 0% N2 | 0.2386 | 0.29993 | 0.79231 | 3.499 | 36.6298 | 47.8127 | 56.1166 | 56.1166 | 55.1174 | 52.6924 | 39.4945 | 26.3284 | 22.3142 | 4.9128 | 0.4171 | 0.24359
15,000 Feet, 20% N2 | 0.243 | 0.30501 | 3.4544 | 24.1907 | 44.9906 | 49.4665 | 49.4665 | 46.9252 | 39.3071 | 30.4954 | 14.3851 | 0.2984 | 0.24693
15,000 Feet, 40% N2 | 0.2027 | 0.28868 | 2.9 | 30.8895 | 39.8982 | 39.8982 | 39.0495 | 30.5682 | 21.6368 | 0.78393 | 0.35743 | 0.2748 | 0.20665
15,000 Feet, 60% N2 | 0.16666 | 0.27757 | 2.944 | 17.4154 | 25.511 | 25.511 | 20.6775 | 4.3067 | 0.2661 | 0.23868
30,000 Feet, 0% N2 | 0.10035 | 0.14461 | 0.39384 | 2.9286 | 18.2807 | 25.1938 | 29.414 | 29.414 | 28.6444 | 25.8557 | 20.8424 | 12.753 | 10.8923 | 0.094817
30,000 Feet, 20% N2 | 0.11082 | 0.14933 | 2.1473 | 17.0611 | 23.1194 | 25.4151 | 25.543 | 25.543 | 24.7288 | 20.7642 | 15.9286 | 10.4751 | 0.16113 | 0.069305
30,000 Feet, 40% N2 | 0.11177 | 0.13924 | 1.9972 | 15.7848 | 20.6114 | 20.6114 | 20.2204 | 16.0733 | 11.4336 | 2.8086 | 0.15524 | 0.085385
30,000 Feet, 60% N2 | 0.047235 | 0.1433 | 2 | 9.0395 | 13.42 | 13.42 | 13.3987 | 8.7159 | 2.0889 | 0.21989 | 0.12244
As altitude increased, limits widened but peak pressure decreased

## Slide 25
Chart: Limiting Oxygen Concentration vs. Pressure
| 3.694626327252927E-2 | 3.7782658959537578E-2 | 3.8262104187946878E-2 | 3.9982764481914602E-2 | 4.1013302939575391E-2 | 4.203398421553952E-2 | 4.2988607767122357E-2 | 4.5022184416468179E-2 | 4.5988847330839855E-2
Atmospheric | 0.012149 | 0.013254 | 0.013878 | 0.017786 | 0.022441 | 0.028065 | 0.037373 | 0.070323 | 0.16772
15,000 Feet | 0.016767 | 0.020002 | 0.021921 | 0.025121 | 0.029493 | 0.028919 | 0.031677 | 0.042978 | 0.054291 | 0.088268 | 0.15969
30,000 Feet | 0.018431 | 0.021866 | 0.027341 | 0.026807 | 0.033916 | 0.050079 | 0.075017 | 0.13038 | 0.20034
40,000 Feet | 0.016069 | 0.022178 | 0.029536 | 0.030888 | 0.033273 | 0.037491 | 0.055479 | 0.084853 | 0.14451 | 0.25304
Less oxygen was needed to ignite at high altitudes

## Slide 26
Chart: Limiting Oxygen Concentration
| 0 | 15000 | 30000 | 40000
Limiting O2 % | 0.0421 | 0.0389 | 0.0361 | 0.0349
Elevation | Limiting O2 %
0 | 4.21%
15000 | 3.89%
30000 | 3.61%
40000 | 3.49%
Limiting oxygen concentration decreased as altitude increased

## Slide 27
Limits of flammability widen as altitude increases

## Slide 28: Conclusion and Future Work
H2 flammability limits widen at high altitude
H2 requires less O2 to ignite at high altitudes, so more N2 is required to inert it
Less powerful explosions at high altitude
Higher spark energy may be needed near upper flammability limits at high altitude