## Slide 1
Julie Mansfield, PhD & John Bolte IV, PhD
The Ohio State University
Collaborators: Amanda Taylor (FAA), Aditya Belwadi (CHOP), Hans Hauschild (MCW)
Pediatric response to oblique loading in aircraft seats with standard and inflatable seat belts

## Slide 2
CChIPS:
Center for Child Injury Prevention Studies

## Slide 4
https://www.faa.gov/travelers/fly_children/
Background

## Slide 5: Background
CRS Regulations –
  Inversion test to ensure occupant is contained during turbulence
  FMVSS 213: CRS are crashworthy in frontal crash scenario
Adult seating is evolving:
  Seats oriented at oblique angles
  Inflatable lap and/or shoulder belts

## Slide 6: Broad goals
Inform policies and regulations of the FAA regarding Child Restraint System (CRS) use on aircraft with obliquely oriented passenger seats and/or inflatable seat belts.
Positive outcomes could allow the FAA to better accommodate families and advise best practices for families traveling with children in CRS.

## Slide 7: Specific Aims
To determine differences in pediatric occupant response for:
Aircraft seats oriented at 30° vs. 45° from the aircraft’s centerline
Standard aircraft lap belts vs. deactivated inflatable lap belts
0°
30°
45°

## Slide 8: Previous testing
2015-2016 CChIPS Study
  Aditya Belwadi (CHOP) and Hans Hauschild (MCW)
Evaluate durability of rear-facing (RF) CRS and forward-facing (FF) CRS installed with inflatable seatbelts under static deployment

## Slide 9: Previous testing
2015-2016 CChIPS Study
  Aditya Belwadi (CHOP) and Hans Hauschild (MCW)
Evaluate durability of rear-facing (RF) CRS and forward-facing (FF) CRS installed with inflatable seatbelts under static deployment
AMSAFE Aviation Inflatable Restraint (AAIR)

## Slide 10: Previous testing
2015-2016 CChIPS Study
  Aditya Belwadi (CHOP) and Hans Hauschild (MCW)
Evaluate durability of rear-facing (RF) CRS and forward-facing (FF) CRS installed with inflatable seatbelts under static deployment
  RF CRS could not be installed properly
    Inflatable belt was too thick to route through base
    Tested without base
    Seat deemed durable

## Slide 11: Previous testing
2015-2016 CChIPS Study
  Aditya Belwadi (CHOP) and Hans Hauschild (MCW)
Evaluate durability of rear-facing (RF) CRS and forward-facing (FF) CRS installed with inflatable seatbelts under static deployment
  RF CRS could not be installed properly
    Inflatable belt was too thick to route through base
    Tested without base
    Seat deemed durable
  FF CRS
    Properly installed
    Substantial lateral tipping
    Seat deemed durable

## Slide 12: Methods: Sled series
Total of 43 tests
FAA Civil Aerospace Medical Institute, Oklahoma City
  Led and supervised by Amanda Taylor (FAA)
    Analysis, Part 1: Aditya Belwadi (CHOP), Hans Hauschild (MCW)
    Analysis, Part 2: John Bolte (OSU), Julie Mansfield (OSU)
16 G, 44 ft/sec triangular pulse (14 CFR Part 25.562)

## Slide 13: Methods: Sled series
Total of 43 tests
FAA Civil Aerospace Medical Institute, Oklahoma City
  Led and supervised by Amanda Taylor (FAA)
    Analysis, Part 1: Aditya Belwadi (CHOP), Hans Hauschild (MCW)
    Analysis, Part 2: John Bolte (OSU), Julie Mansfield (OSU)
16 G, 44 ft/sec triangular pulse (14 CFR Part 25.562)
Variable | Conditions
Aircraft seat orientation angle | 30° or 45° from centerline
Type of lap belt | Deactivated inflatable or standard
CRS and ATD | RF (Q1), FF (HIII 3yo), or No CRS (HIII 3yo)
Adjacent structure | Wall, armrest, or no barrier

## Slide 14: Methods: Sled series
FF
No CRS
No barrier
ARmrest
RF
Wall

## Slide 15: Methods: ATD Instrumentation
Q1
  3a⍵ - head
  Tri-axial accels - pelvis
  6-axis upper neck load cell
  Thoracic potentiometer
HIII 3 year-old
  3a⍵ - head
  Tri-axial accels
    T1, T12,Chest & Pelvis
  6-axis upper neck load cell
  Thoracic potentiometer
  2-axis ASIS load cell
  2-axis Pubic load cell

## Slide 16: Results: 45°, FF CRS – HIII 3YO
Armrest
Wall
No Barrier

## Slide 17: Results: 45°, No CRS - HIII 3YO
Armrest
Wall
No Barrier

## Slide 18: Results: 45°, RF CRS – Q1
Armrest
Wall
No Barrier

## Slide 19: Specific Aims
To determine differences in pediatric occupant response for:
Aircraft seats oriented at 30° vs. 45° from the aircraft’s centerline
Standard lap belts vs. deactivated inflatable lap belts

## Slide 20: Key
Belt type
St = Standard lap belt
In = Inflatable lap belt (deactivated)
Adjacent structures
NoB = No barrier
Arm = Armrest
Wal = Wall

## Slide 21: results: HIC 15
  IARVs
    568 for HIII 3YO
    389 for Q1
* Head strike

## Slide 22: results: HIC 15
  IARVs
    568 for HIII 3YO
    389 for Q1
* Head strike

## Slide 23: results: Thoracic deflection
  IARVs
    1.1” for HIII 3YO
    0.9” for Q1

## Slide 24: results: Neck Injury Criterion (Nte)
  IARV
    1.0 for all

## Slide 25: results: Neck Injury Criterion (Ntf)
  IARV
    1.0 for all

## Slide 26: results: Left Belt force

## Slide 27: Specific Aims
To determine differences in pediatric occupant response for:
Aircraft seats oriented at 30° vs. 45° from the aircraft’s centerline
Standard lap belts vs. deactivated inflatable lap belts

## Slide 28: Specific Aims
To determine differences in pediatric occupant response for:
Aircraft seats oriented at 30° vs. 45° from the aircraft’s centerline
Standard lap belts vs. deactivated inflatable lap belts
*Results presented for 45° tests only*

## Slide 29: results: HIC 15
  IARVS
    568 for HIII 3YO
    389 for Q1

## Slide 30: results: Thoracic deflection
  IARVs
    1.1” for HIII 3YO
    0.9” for Q1

## Slide 31: results: Neck Injury Criterion (Nte)
  IARV
    1.0 for all

## Slide 32: results: Neck Injury Criterion (Ntf)
  IARV
    1.0 for all

## Slide 33: results: Left Belt force

## Slide 34: Conclusions
Aim 1 – 30° vs. 45° oblique angle
  Chest deflection
    Greater for 30º than 45º conditions
  Neck Injury Criteria
    NTE & NTF – Similar across 30º and 45º
  HIC15
    Head strikes in several 45° conditions
    No head strikes in 30° conditions
  Consider limiting the offset angle at which pediatric passengers can be seated, particularly when adjacent structures could pose the threat of head strikes.
Aim 2 – Standard vs. deactivated inflatable lap belts
  Issues installing RF CRS with base
  Once installed, similar performance across belt types

## Slide 35: Conclusions
These data support the FAA’s recommendation to use CRS on aircraft whenever possible.
Benefits of rear-facing CRS are especially prominent when considering head containment and head protection.

## Slide 36: Acknowledgements
Primary Mentor
  Amanda Taylor – FAA
Collaborators
  Aditya Belwadi – Children’s Hospital of Philadelphia
  Hans Hauschild – Medical College of Wisconsin
CChIPS Mentors
  Hyunjung Kwon – TRC Inc.
  Hiro Tanji – Takata
  Jerry Wang – Humanetics
  Eric Dahle – Evenflo/Goodbaby
OSU Students
  Colleen Harkins
  Sarah Shaffer
  Gina Gugliotta
  Abbey Barnette

## Slide 37
Julie Mansfield, PhD & John Bolte IV, PhD
The Ohio State University
Collaborators: Amanda Taylor (FAA), Aditya Belwadi (CHOP), Hans Hauschild (MCW)
Pediatric response to oblique loading in aircraft seats with standard and inflatable seat belts

## Slide 38: Sled pulse
16 G, 44 ft/sec triangular pulse (14 CFR Part 25.562)

## Slide 39: Head strikes

## Slide 40: Head strikes

## Slide 41: Test matrix: 30° tests

## Slide 42: Test matrix: 45° tests

## Slide 43: 45° tests With head strikes