## Slide 1: SAE A-22 and ac20-135 revision AS6826/3 Fire Test Pass/Fail Criteria for Powerplant and Propulsion System Components INTERNATIONAL AIRCRAFT SYSTEMS FIRE PROTECTION FORUM
  October 29th, 2019
  Daniel Laborie (GE Aviation) & Paul Wittman (ST Engineering)

## Slide 2: Scope of new Aerospace Standard AS6826/3
Powerplant and propulsion system components are required to carry a satisfactory level of fire resistance. The fire resistance requirements are defined in various FAA publications. Compliance demonstration can be done through various approaches (description, analysis, test, etc.).
When compliance is claimed by test, there is a need to define clear and determinate pass/fail criteria to provide the fire test laboratory a means of evaluating success without any ambiguity.

## Slide 3: Approach
Document will provide specific pass-fail criteria for the various components of a powerplant
Firewall, fire barrier between different zones
Fire extinguishing lines
Fire detectors
Engine/ APU mounts
Nacelle latches and hinges
Fire seals
Flammable-fluid carrying piping, hoses and components
Air-carrying components
Electrical wires and connectors
Electronic components
Surfaces to the rear of the nacelles

## Slide 4: Key Points
Criteria will point to alternates based on previously FAA or EASA accepted approaches that are publicly available (AC, AMC, ELOS, ESF, …) when applicable
Residual flame (after removal of the burner): acceptability will be dependant on the type of component and on risk to the surrounding environment
Since residual flames may occur on multiple components of a single fire zone, the process will require an overall assessment of the acceptability of such outcome for the fire safety of the installation
Upon application of the burner flame, there may be a temporary increase of the flame pattern. The document will provide some criteria for acceptance (or rejection)
A draft (and incomplete) version of this AS is available on the SAE A-22 website

## Slide 5: SAE A-22 and ac20-135 revision AS6828 Fire HAZARD ASSESSMENT for Powerplant and Propulsion System Components INTERNATIONAL AIRCRAFT SYSTEMS FIRE PROTECTION FORUM
  October 29th, 2019
  Daniel Laborie (GE Aviation) & Paul Wittman (ST Engineering)

## Slide 6: Scope of new Aerospace Information Report AS6828
Scope of this document has been changed:
The original concept of assessing the acceptability of a given fire test based on a risk analysis was rejected by the airworthiness authorities
However, it was felt that the draft document contained valuable information and that a template for performing a risk analysis at the installation level would be valuable for the industry
This AIR will also document publicly available ELOS or ESF as potential alternates to AS6826/3 pass-fail criteria
Thus, the scope of the document will tentatively focus on a (fire) risk analysis at the installation level
A draft version of this AIR is available on the SAE A-22 website and will require significant work. Its publication will be scheduled after the other AS documents.