## Slide 1: 747 Hidden Fire 2-BTP Testing Systems Working Group Meeting Long Beach, CA
Robert Morrison
November 14 - 15, 2012

## Slide 2: Background
November 2011 System’s Meeting Presentation
  Presentation on “Analysis of Suppressant‐Enhanced Overpressure in the FAA Aerosol Can Simulator” eluded to the possibility that 2-BTP (2-Bromo-3,3,3-Trifluoropropene) may contribute hydrocarbons to a fire threat
  The analysis covered BTP in a pressurized environment
  This raised questions about how low of a pressure would BTP exhibit this behavior
FAA Technical Center Meeting
  The FAA, Boeing, and American Pacific discussed the merits of BTP’s decomposition product behavior
  FAA requested to test BTP in a hidden fire scenario to view its behavior in a real environment

## Slide 3: Test Article - Boeing 747SP Aircraft
A145 ft3 area on the left side of the nose landing gear wheel well area, forward of the electronics and equipment (E&E) bay, between Stations 260 and 340 was selected as the test section
This area afforded easy access for instrumentation, project equipment, and emergency response
  First Class cabin floor access door to E&E bay
  Forward Electronic Access Door behind Nose Gear
    Both access doors near Station 420

## Slide 4: 2-BTP Testing
Problem Overview
  Does BTP contribute hydrocarbons (decomposition products) to the fire threat when there isn’t enough BTP present to put out a standard hidden fire test block
2 test scenarios
  Suppressed, extinguisher discharge at Station 305 vent
  Non-suppressed, extinguisher discharge at Station 290 vent
Fire Threat
  Standardized (hidden fire) 4” x 4” x 9” polyurethane foam block
  Installed in a 12” x 14” x 20” fire hardened box
    Box is open on 3 sides – windows with 1” frame border
  Foam block is centered on the 12” x 14” base
  Accelerant – 10 cc Heptane
  Fire box position is hung 13” below the First Class Cabin floor at Station 310 with the base plate 7 ½” from the outer skin

## Slide 9
Station 305

## Slide 11
Station 305
Station 290

## Slide 13: Test Collection
3 Video Channels
  Fire Box – wide angle, high resolution
  Fire Box – high zoom, high definition
  Fire Fighter – wide angle, high resolution
5 Channels
  Carbon Monoxide, 0 – 2%
  Carbon Dioxide, 0 – 10%
  Halon 1211, 0 – 30%
  Oxygen, 0 – 25%
  Total Hydrocarbon, 0 – 4%

## Slide 14
Test #2
Test #8
BTP – Non-Suppressed
BTP – Suppressed

## Slide 15
Chart: 2-BTP Total Hydrocarbons

## Slide 16
Chart: 2-BTP Total Hydrocarbons

## Slide 17: Summary of Results
  Video data suggests that BTP does not contribute flammable hydrocarbons or add energy to the fire threat when there isn’t enough agent present to put the fire out (at 1 atm)
  THC data supports that BTP does produce hydrocarbons as a decomposition product
    Further calibration needed to explain or rule out the peaks starting with neat agent
    Hypothesis is that the analyzer is picking up BTP’s extra carbon atoms
  A restriction was found in the 5 channel gas analyzer post test
    Plan to re-run the Halon test series for validation
    This will determine the amount of retesting