## Slide 1: Smoke Source Project
Robert Morrison, FAA Technical Center Fire Safety
October 21 - 22, 2015
Systems Working Group Meeting Atlantic City, New Jersey

## Slide 2: Background
The objective is to compare different theatrical smoke generating smoke sources to a 4800 lithium primary battery fire test performed in a Class E cargo compartment that resulted in completely obscuring the flight deck in as little as 16 minutes on a Boeing 727 aircraft.
Harry Webster’s February 26, 2013 Lithium Battery Test Video

## Slide 3: Project Work
Two smoke sources are being evaluated
ViCOUNT SDT theatrical smoke generator series
  CO2 injection with 1, 2, 3, & 4 heater bars
  Helium injection with 1, 2, 3, & 4 heater bars
Rosco 1700 theatrical smoke generator with FAA Helium injection box series
  70/30 Helium/Air mix
  50/50 Helium/Air mix
  0/100 Helium/Air mix

## Slide 4
Smoke tests are being conducted in the
FAA Seat Toxicity Test section inside the TC-10 test article.
Smoke machine positioned against orange kick board replacing the Fire Fighter.

## Slide 5: Test Set Up
4 Smoke Meters used to measure smoke plume speed across a total of 16.535 feet
4.75’
6.875’
4.91’

## Slide 6: Testing Results

## Slide 7: Planned Work
Rosco 1700 theatrical smoke generator with FAA Helium injection box series
  70/30 Helium/Air mix
  50/50 Helium/Air mix
  0/100 Helium/Air mix
Findings will determine next course of action.
Possible adjustments
  Heating FAA Helium Box chimney
  Changing to a higher output Rosco generator
Contact Info & Questions: robert.morrison@faa.gov (609) 485-4507