## Slide 1
Smoke Transport Modeling in Cargo Bays
Parametric Study
Changmin Cao, May Corn, Vaidya Sankaran
United Technologies Research Center
Kenneth Bell, Amanda Daly, Terry Simpson
Kidde Fire Protection Systems
International Aircraft Systems Fire Protection Forum
Atlantic City, NJ
October 31st – Nov 1st , 2018
This document has been publicly released and is not subject to export controls.

## Slide 2: Detection system design
Objective: Develop a model-based tool to augment & streamline certification process
Benefits:
Virtual tests
Parametric variations
Physical insight
Accelerate design & development
Cargo Bay Detection System Design Tool
Reduce number of flight certification tests
Reduce cost of certification
This page does not contain any export controlled technical data.

## Slide 3: Model components
1. Smoke Generator
Size distribution
Temperature, Velocity
Turbulence
2. Smoke Transport
Large room features / obstructions
Small scale features – detector tray
Buoyancy, Ventilation
Environmental conditions
3. System Response Time
Obscuration (smoke concentration) & entry time
What sub-elements or components are needed for a model-based design tool ?
  Recap from May 2018:
  Method for simulating a smoke generator
  Methodology to simulate smoke transport in an affordable manner
  Demonstrated this method in a cargo bay (image shown above)
  FAA Systems WG Meeting – Cologne, Germany
This page does not contain any export controlled technical data.

## Slide 4: Model components
1. Smoke Generator
Size distribution
Temperature, Velocity
Turbulence
2. Smoke Transport
Large room features / obstructions
Small scale features – detector tray
Buoyancy, Ventilation
Environmental conditions
3. System Response Time
Obscuration (smoke concentration) & entry time
What sub-elements or components are needed for a model-based design tool ?
  Today’s focus:
  Parametric assessment of smoke generator
  System response time
  FAA Systems WG Meeting – Atlantic City, New Jersey
This page does not contain any export controlled technical data.

## Slide 5: MOTIVATION: Smoke generator characterization
Why should we characterize Smoke Generator ?
Smoke Generator A
Low velocity undulating plume vs. high velocity turbulent plume
Higher ambient T (& low density) not effective in plume slow down & lateral mixing
Buoyancy effects of the (hot) plume can change smoke transport
Smoke Generator inlet conditions affects smoke transport & detector response
Smoke Generator B
Higher Velocity,
Higher Temperature
This page does not contain any export controlled technical data.

## Slide 6: Design - Simulation tool
3-D, unsteady solver
Large Eddy Simulation (LES)
Low Mach with Direct Poisson equation solver for pressure
Time Integration: 2nd order explicit predictor-corrector scheme
Model Cargo Bay
Tool simulates multiple design in a day – parallel execution
SD2
SD1
SD3
SD4
Vary smoke generator & detector position along with other relevant geometrical / flow parameters
Select promising designs to test
Fire Dynamics Simulator
This page does not contain any export controlled technical data.

## Slide 7: Baseline case 1: Smoke gen A
Temperature (0C)
Obscuration (%/m)
SD2
SD1
SD3
SD4
Temperature and obscuration profiles follow expected trends
Case Smoke Generator & Ambient Condition | 
1 | Baseline SG conditions: STP – Ambient
2 | Higher velocity (V) compared to baseline: STP (Ambient)
3 | Higher V & T compared to baseline: STP (ambient)
4 | Baseline SG conditions: Lower ambient pressure
5 | Baseline SG conditions STP (ambient): With cross ventilation
Once the smoke reaches the detector smoke concentration increase quickly and reaches stable value
This page does not contain any export controlled technical data.

## Slide 8: Baseline case 1: alarm time
Activation Obscuration | SD1 | SD2 | SD3 | SD4
3.2 %/m (1 %/ft) | 52.2 | 23.0 | 27.2 | 48.2
10 %/m (3 %/ft) | 52.8 | 23.2 | 27.4 | 48.6
Predicted Smoke detector alarm time (s) at different obscuration levels
3.2%/m
10%/m
Calibrates to experimental data (e.g., same order of magnitude)
Calibrate alarm time using experimental data
This page does not contain any export controlled technical data.

## Slide 9: BASELINE vs. Higher t smoke gen.
Case 1: Baseline Smoke Gen A
Smoke generator input conditions impact the plume dispersion to the detectors
Case 3: Smoke Gen B
Effect of higher heat input (temperature) to smoke generator
SD2
SD1
SD3
SD4
Case Smoke Generator & Ambient Condition | 
1 | Baseline SG conditions: STP – Ambient
2 | Higher velocity (V) compared to baseline: STP (Ambient)
3 | Higher V & T compared to baseline: STP (ambient)
4 | Baseline SG conditions: Lower ambient pressure
5 | Baseline SG conditions STP (ambient): With cross ventilation
This page does not contain any export controlled technical data.

## Slide 10
Case 1 | Smoke Generator A
Case 2 | Temperature from Smoke Generator A Velocity from Smoke Generator B
Case 3 | Smoke Generator B
Tool can be used to conduct controlled parametric variations for
design analysis and to understand system response
Parametric study for different scenarios: Alarm time comparisons
BASELINE vs. Higher temperature sg
This page does not contain any export controlled technical data.

## Slide 11: Extensions to other scenarios
Case 1 | Smoke Generator A at STP
Case 4 | Smoke Generator A at In-Flight ambient Conditions
Case 5 | Smoke Generator A at STP with Ventilation
Smoke arrival time changes in flight and ventilation cases
Ventilation accelerates smoke spread and reduces detector alarm time (for this design)
SD2
SD1
SD3
SD4
Case 4: In-flight condition
Case 5: with ventilation
Parametric study for different scenarios: Alarm time comparisons
This page does not contain any export controlled technical data.

## Slide 12: Summary and Next steps
Smoke transport simulations capture the effect of different smoke generators
  Models demonstrate encouraging ability to capture parametric sensitivity
  Linking detector model to the smoke transport is key to accurately predict alarm time
Modeling capability to simulate real-scale cargo-bay with varied input conditions
  Ability to perform “virtual tests” to reduce cost of design / certification
  Approximately 20 to 30 cases / conditions / designs can be simulated in a week
Next step: Acquiring data to validate transport/detector models for the cargo bay
Kidde Fire Protection Systems - Cargo Bay Test Simulator
This page does not contain any export controlled technical data.